## Slide 1: Management of Networks with Constrained Devices: Use Cases
Dan Romascanu
dromasca@avaya.com

## Slide 2: What is COMAN
IETF non-WG activity focused on Management of Networks with Constrained Devices
  Active 2011-2014 as a non-WG team
  Final phase of work in the OPSAWG for broader community exposure
  Two RFCs:
    Management of Networks with Constrained Devices: Problem Statement and Requirements - http://www.rfc-editor.org/rfc/rfc7547.txt
    Management of Networks with Constrained Devices: Use Cases - http://www.rfc-editor.org/rfc/rfc7548.txt

## Slide 3: RFC 7547
The definition of ‘constrained devices’ is taken by reference from RFC 7228 ‘Terminology for Constrained-Node Networks’ - http://www.rfc-editor.org/rfc/rfc7228.txt
  ‘Small devices with limited CPU, memory, and power resources, so- called "constrained devices" (often used as sensors/actuators, smart objects, or smart devices) can form a network, becoming "constrained nodes" in that network. Such a network may itself exhibit constraints, e.g., with unreliable or lossy channels, limited and unpredictable bandwidth, and a highly dynamic topology.’
Also from RFC 7228 – definitions of classes of constrained devices
  C0: data size (e.g., RAM) << 10 KiB; code size (e.g., Flash) << 100 KiB
  C1: data size (e.g., RAM) ~ 10 KiB ; code size (e.g., Flash) ~ 100 KiB
  C2: data size (e.g., RAM) ~ 50 KiB; code size (e.g., Flash) ~ 250 KiB
Introduces 7 classes of Configuration Management and 4 classes of Monitoring Support
Problem Statement: answer the ‘need to reconsider the network management mechanisms based on the new, changed, and reduced requirements coming from smart devices and the network of such constrained devices…the management of a network with constrained devices is necessarily designed in a simplified and less complex manner.’
Requirements for:
  Management Architecture/System
  Management Protocols and Data Models
  Configuration Management
  Monitoring Functionality
  Self-Management
  Security and Access Control
  Energy Management
  Software Distribution
  Traffic Management
  Transport Layer
  Implementation Requirements

## Slide 4: RFC 7548 – Use Cases (1)
Environmental Monitoring
  Environmental monitoring applications are characterized by the deployment of a number of sensors to monitor emissions, water quality, or even the movements and habits of wildlife. Other applications in this category include earthquake or tsunami early- warning systems. The sensors often span a large geographic area; they can be mobile; and they are often difficult to replace. Furthermore, the sensors are usually not protected against tampering.
  Management of environmental-monitoring applications is largely concerned with monitoring whether the system is still functional and the roll out of new constrained devices in case the system loses too much of its structure.
Infrastructure Monitoring
  Infrastructure monitoring is concerned with the monitoring of infrastructures such as bridges, railway tracks, or (offshore) windmills. The primary goal is usually to detect any events or changes of the structural conditions that can impact the risk and safety of the infrastructure being monitored. Another secondary goal is to schedule repair and maintenance activities in a cost-effective manner.
  The management of infrastructure monitoring applications is primarily concerned with the monitoring of the functioning of the system. Infrastructure monitoring devices are typically rolled out and installed by dedicated experts, and updates are rare since the infrastructure itself does not change often. However, monitoring devices are often deployed in unsupervised environments; hence, special attention must be given to protecting the devices from being modified.

## Slide 5: RFC 7548 – Use Cases (2)
Industrial Applications
  Industrial Applications and smart manufacturing refer to tasks such as networked control and monitoring of manufacturing equipment, asset and situation management, or manufacturing process control. … Potential industrial applications (e.g., for smart factories and smart manufacturing) are:
    Digital control systems with embedded, automated process controls; operator tools; and service information systems optimizing plant operations and safety.
    Asset management using predictive maintenance tools, statistical evaluation, and measurements maximizing plant reliability.
    Smart sensors detecting anomalies to avoid abnormal or catastrophic events.
    Smart systems integrated within the industrial energy-management system and externally with the smart grid enabling real-time energy optimization.
  Management of industrial and factory applications is largely focused on monitoring whether the system is still functional, real-time continuous performance monitoring, and optimization as necessary. The factory network might be part of a campus network or connected to the Internet. The constrained devices in such a network need to be able to establish configuration themselves (autoconfiguration) and might need to deal with error conditions as much as possible locally. Access control has to be provided with multi-level administrative access and security. Support and diagnostics can be provided through remote monitoring access centralized outside of the factory.
Energy Management
  Another IETF WG (EMAN) developed an energy-management framework [RFC7326]
  a power distribution network is responsible for the supply of energy to various devices and components, while a separate communication network is typically used to monitor and control the power distribution network. Devices in the context of energy management can be monitored for parameters like power, energy, demand and power quality. If a device contains batteries, they can be also monitored and managed.
  Smart Grid - an electrical grid that uses data networks to gather and act on energy and power-related information in an automated fashion with the goal to improve the efficiency, reliability, economics, and sustainability of the production and distribution of electricity.
    Smart Metering
    An Advanced Metering Infrastructure (AMI) network enables an electric utility to retrieve frequent electric usage data from each electric meter installed at a customer's home or business.

## Slide 6: RFC 7548 – Use Cases (3)
Medical Applications
  remote health-monitoring and emergency- notification systems
  medical sensors attached to human bodies, or installed in the infrastructure used by humans
  need to protect the safety and privacy of the people who use medical devices
  timely delivery of data
  fault detection of the communication network or the constrained devices
Building Automation
  the distributed systems designed and deployed to monitor and control the mechanical, electrical, and electronic systems inside buildings with various destinations … Advanced Building Automation Systems (BASs) may be deployed concentrating the various functions of safety, environmental control, occupancy, and security.
  High priority on safety and security. Management systems must be resilient to events like loss of power or security attacks, must be able to deal with unintentional segmentation of networks due to power loss or channel unavailability, and must also be able to detect security events.

## Slide 7: RFC 7548 (4)
Home Automation
  includes the control of lighting, heating, ventilation, air conditioning, appliances, entertainment and home security devices to improve convenience, comfort, energy efficiency, and safety. It can be seen as a residential extension of building automation … operated in a considerably more ad hoc manner.
  The management responsibility either lies with the residents or is outsourced to electricians and/or third parties providing management of home-automation solutions as a service … The time scale for failure detection and resolution is, in many cases, likely counted in hours to days.
Transport Applications
  generic term for the integrated application of communications, control, and information processing in a transportation system
    inter- and intra-vehicular communication, smart traffic control, smart parking, electronic toll-collection systems, logistic and fleet management, vehicle control, and safety and roadside assistance.
  High distribution and mobility of the devices
  High priority on safety
  High availability and self-repair capabilities

## Slide 8: RFC 7548 (5)
Community Network Applications
  constrained routers in a multi- hop mesh topology, communicating over lossy, and often wireless, channels. While the routers are mostly non-mobile, the topology may be very dynamic because of fluctuations in link quality of the (wireless) channel. Used for various applications like location-based services, free Internet access, file sharing between users, distributed chat services, social networking, video sharing, etc.
  require an ad hoc routing protocol that allows for quick convergence to reflect the effective topology of the network
    No human intervention is required, however, external management and monitoring of an ad hoc routing protocol may be desirable to optimize parameters of the routing protocol.
Field Operations
  mission-critical networks operated in the field by rescue and security agencies
  fixed NOC, pre-configured devices, configuration changes required would need to be appropriately encrypted and authenticated to prevent unauthorized access.
  hostile environments, a high failure and disconnection rate should be tolerated by the NMS, which must also be able to deal with multiple gateways and disjoint management protocols.