Proposal to 7478

(Same principle applies to 7587 and new texts to spec are in red)

- Change the following schema in Section 4.1 of WS-Eventing

[Action]

http://www.w3.org/2009/02/ws-evt/Subscribe

[Body]

<wse:Subscribe ...>

<wse:EndTo> endpoint-reference </wse:EndTo> ?

<wse:Delivery ...> xs:any* </wse:Delivery>

<wse:Format Name="xs:anyURI"? > xs:any* </wse:Format> ?

<wse:Expires Exact="xs:boolean"?> (xs:dateTime | xs:duration) </wse:Expires> ?

<wse:Filter Dialect="xs:anyURI"? ...> xs:any* </wse:Filter> ?

xs:any*

</wse:Subscribe>

2. Add the following paragraphs to Section 4.1 of WS-Eventing

[Body]/wse:Subscribe/wse:Expires@Exact

If this optional attribute has value “true”, then the Event Source MUST either create a subscription with the requested expiration time or reject the request due to an expiration time that cannot be supported. If the request is rejected, the Event Source MUST generate a wse:ExpirationTimeExceeded fault.

Implied value of this optional attribute is “false” where the event source defines the actual expiration as described in [Body]/wse:Subscribe/wse:Expires.

3. Add the following Fault specification

6.x ExpirationTimeExceeded

This fault is generated when a Subscribe request specifies an expiration time with wse:Subscribe/wse:Expires@Exact  value “true” that exceeds what the Event Source is willing to support.

[Code]

s12:Sender

[Subcode]

wse:ExpirationTimeExceeded

[Reason]

The requested expiration time exceeds internal limits

[Code]

Optional xs:duration which specified the maximum expiration time supported by the Event Source.

4. Similar Changes for “Renew” following the same approach as described in (2).