## Slide 1
IFSF Limited
Mobile Payment – Pay at Pump
John Carrier, Projects Manager

## Slide 2
Architecture Overview
PCI Relevant
NB: These are Logical Components
CHP
Card
Acquirer
FEP/ SWITCH
M-PAY
Site Computer
FDC
Forecourt Network
Fuelling
Point 1
Dispenser/Calculator
Fuelling
Point 2
POS
Server
Sales
Application
Card
Issuer
Site LAN
POS Terminal
Vehicle
MPPA
Cloud/WAN
Network
Cloud/WAN
Network
ISO8583Oil
H2H
ISO8583Oil
P2F
IFSF FDC to POS
(Web)
IFSF FDC to POS
(TCP-IP)
ISO8583Oil
P2H
VISS Console
MP
App.
Mobile Data Network
MP
App.
Smart Phone
Charging
Point 1
Dispenser/Calculator
Charging
Point 2
M-PAY
SITES WAN
Network

## Slide 3
Architecture Overview
PCI Relevant
NB: These are Logical Components
CHP
Card
Acquirer
FEP/ SWITCH
M-PAY
Site Computer
FDC
Forecourt Network
Fuelling
Point 1
Dispenser/Calculator
Fuelling
Point 2
POS
Server
Sales
Application
Card
Issuer
Site LAN
POS Terminal
Vehicle
MPPA
Cloud/WAN
Network
Cloud/WAN
Network
ISO8583Oil
H2H
ISO8583Oil
P2F
IFSF FDC to POS
(Web)
IFSF FDC to POS
(TCP-IP)
ISO8583Oil
P2H
VISS Console
MP
App.
Mobile Data Network
MP
App.
Smart Phone
Charging
Point 1
Dispenser/Calculator
Charging
Point 2
M-PAY
SITES WAN
Network
W3C #autopay
scope

## Slide 4
Architecture Walkthrough
@IFSFonline
For example – many missing applications
  Sites geo-location database interface
  Site Products database
  Payments system Sites interface
  Payment systems Customer account interface
  Loyalty processing and Electronic Loyalty Servers
  Security (Certificates/firewalls/encryption/etc.,)
  Car parking, Road Tolls, bridges, tunnels and ferries
  Car valeting (incl. tyre pressure)
NB: The above list is incomplete
Very Important Point
- highly simplified diagram

## Slide 5
Happy Path Walkthrough
Fuelling point (i.e. service delivery point) knows where it is
“Mobile device” (Phone, vehicle, tablet) knows where it is
Payment (account) available and default known
Max fuelling amount pre-set (e.g. $50)
All Application WAN and Site LAN networks functioning
Fuelling Pump is Idle (nozzle up) and Ready (zero memory)
Available and required “Product Grades” known
Loyalty Identifier known and enabled
Robotic fuelling and Wireless charging is not yet available
Selected Fuelling Point cannot be uniquely identified
Prerequisites
- In order to minimise dialogue

## Slide 6
Happy Path Walkthrough
@IFSFonline
Three “Success” API Messages
  Reserve Fuelling Point
  Approve Fuelling Point (following account authorisation)
  Completed Fuelling Transaction (the sales and delivery receipt)
Two “Failure” API Messages
  Free Fuelling Point
  Cancel Fuelling Transaction (following account authorisation)
API Summary
- If all goes to plan!!

## Slide 7
Sad Path Walkthrough
@IFSFonline
>95% of transactions follow happy path but….
  The sad path can be hugely problematic and difficult to fix
  At least 22 “Sad” paths identified and need thorough testing
Two “Failure” API Messages
  Cancel Fuelling Point (to “Un-authorise” a pre-authorised account payment)
  Free Fuelling Point (to un-reserve a Fuelling point after a User, Systems or operator intervention/error)
And ”many timers” required – esp. related to connectivity and user operational issues
  E.g. no Failure message from site
  No Approve message to site
  How long do you wait??? What length of time for a timer?
  Nozzle juggling , mixed service mode complexities (post pay and OPTs at same time)
API Summary
- When something goes wrong

## Slide 8
Alternative Scenarios
@IFSFonline
Conditional Processing
  “Digital Offers” redemption (changes unit price or final sale price)
  Payment account not pre-configured (dynamically selected/entered)
  Acceptable product grade(s) not configured
  Location services not enabled – Service Point needs to be uniquely identified
  First use (Fire and other safety regulations to be followed)
  Local paper receipt required (Trading standards)
Exceptions
  Hardware and mechanical failures (including network WAN and LAN)
  Pump not free, Pump out of order, pump configured wrong
  Insufficient funds in account or account not available
  Operator, cashier, customer, vehicle or “system” aborts transaction
  Incompatible product / grade selected
Conditions and Exceptions

## Slide 9
Misc. Operational Issues
@IFSFonline
Mixed Service Modes
  Cashier needs to know status of the ”Mobile Payment” transaction at all times to reduce “accidental” drive offs (Fuel is taken but not paid for)
  Fuelling Point must handle nozzle juggling (if not robotic or wireless)
  Acceptable product grade(s) not configured
  Fuelling point dynamically (i.e. per transaction) sets unit price and ”service mode”)
Alternative Architectures
  IFSF has identified 5 real-world working architectures – this one is “winning” because
    Site doesn’t require OPT, CRIND or COPT – but does need “unmanned controller device”
    No PCI re-certification of site EPS (or any other connected components) is necessary
    No PCI relevant data (neither sensitive or personal or private) is required to be transmitted to site
    Often referred to as OTA (“over the air” authorisation)
    No OIML nor W&M recertification of site equipment / operations needed
Operational issues

## Slide 10
Shell Fill & Go – Happy Path
@IFSFonline

## Slide 11
Shell Fill & Go – Happy Path
@IFSFonline

## Slide 12
Shell Fill & Go – Happy Path
@IFSFonline

## Slide 13
Shell Fill & Go – Happy Path
@IFSFonline

## Slide 14
Shell Fill & Go – Happy Path
@IFSFonline