## Slide 1: Ideas for Gen2
WS/HTTP alignment of access restriction handling
Access restriction tagging of resources
Array data type

## Slide 2: WS/http access restriction pattern alignment
The request messages over the Websocket protocol has a specific payload for sending the token.
Over HTTP the token is ”inserted” into the get/set request.
The pattern used in HTTP can be modelled on WS by:
  Adding the existing ”tokens” key-value pair as optional in the get/set payloads.
Benefits:
  Same pattern over both protocols.
  Simplifies access restriction server implementation.
Risks:
  Future protocols to be supported may not support the ability to ”insert” token into get/set(/subscribe) requests.
    Can be solved, to the cost of server implementation complexity (in the transport manager for this new protocol).

## Slide 3: Access restriction tagging of resources
The Gen2 server needs to know which resources that require authorization verification before access.
The natural place for this information is in the VSS tree.
Proposal:
  New optional property ”restricted”: ”none”/”write”/”readwrite”
  Only to be used in leaf nodes
  If not present, then there is a default rule.
  Default rule is set in a branch with the property
    ”restricted-default”: ”none”/”write”/”readwrite”
    It is then valid as default for all direct children of this branch
    Default for default is ”none”
      I.e. a tree without any of the mentioned properties has no access restrictions
  Access restriction properties would typically be provisioned to the tree by the OEMs before vehicle deployment.

## Slide 4: Array data type
There is currently no support in VSS for arrays specified in a single node.
This can be supported by the following:
  Adding a new property: ”elements”: X
    X > 1 (default for missing property is ”elements”:1)
  Syntax for the value-property in set request/get response/subscription notification:
    ”value”: [x, y, z,..]