## Slide 1: Location Interface
Proposal :
Remove this interface from Vehicle information API.
Justification :
Already available in W3C Geolocation API : Position.coords
A Genivi API already exists and is more detailled, this should be addressed in the futur navigation working group.

## Slide 2: VehicleSpeed Interface
Proposal :
Remove this interface.
Justification :
Already available in W3C Geolocation API : Position.coords.speed

## Slide 3: Acceleration Interface
Proposal :
Remove this interface.
Justification :
Only if already available in an existing W3C API

## Slide 4: DeadReckoning Interface
Proposal :
Remove this interface.
Justification :
DeadReckoning is not a data but a function.
Needed data (attributs) are not correct (Steering wheel angle not used and wheel tic sensors used are only rear wheels)

## Slide 5: SteeringWheelAngle Interface
Proposal :
Add this interface.
Justification :
Needed for several use cases :
  Drowziness detection
  Maneuver detection

## Slide 6: WheelTicSensors Interface
Proposal :
Add this interface.
Justification :
Needed for several use cases :
  DeadReckoning,
  Slippery road detection,
  Low tire pressure detection, …