## Slide 1: Hypermedia Design for Machine APIs: An Example
Michael J Koster
August 15, 2015

## Slide 2: Hypermedia is Metadata
Application Semantics and Discovery
  Describes intrinsic resources and controls at the application level using physical concepts like temperature, light intensity
  Enables applications to discover the proper resources to link to
API State Machine Automation
  Enables Common Web Client to interact with any device or virtual entity, regardless of schema or model structure, or protocol used
  Hypermedia controls work like HTTP links and forms, but for functional abstractions of physical world items like on/off light switch controls
Context Integration
  Contextual information like installed location, what is being measured and controlled, also used in application resource discovery
Using Web Linking, Relations, and Attributes

## Slide 3: Models and Bindings
Thing Description models are high level abstractions for the Actions, Events, and Properties of things
Action, event, and property resources have defined bindings to M2M APIs, either through common patterns or through specialized interaction templates (like html forms)
High level functional abstractions for controls (Actions in the W3C thing model) map to machine operations at the (REST) API level
Example based on a set of controls for professional lighting
Actions are mapped to operations on IPSO Lighting objects (OnOff, Level, and Color actuators)
Level control (Brightness) object is used as an example

## Slide 4: Lighting Model - Control Actions
light
onOff
level
color
change
toggle
newState:
{enum:off,on}
HS
XY
temperature
change
step
move
targetValue:{units:%}
transitionTime
rate:{units:%/s}
stepSize
stop
transitionTime:{units:s}
change
step
move
targetValue:{units:K,range:2700-5500}
transitionTime
rate:{units:K/s}
stepSize
transitionTime:{units:s}
stop
light.onOff.change
{newState:on}
light.color.temperature.change
{targetValue:2900,transitionTime:10}
light.level.change
{targetValue:45,transitionTime:10}
thing
actuators
actions
parameters
application actions {parameters}
(colorspace)

## Slide 5: IPSO Level Control – Resource Model

## Slide 6: Description => Protocol => Model
Protocol Binding
name
binding
href
datatype
method
mediatype
expects
returns
statuscodes
Semantic Binding, Thing Description
Actions
  action
  binding
  datatype
Events
  Subscribe Bindings
Properties
  Get/Set Bindings
Resource Model
Instances of Schema
O
R
R
R
O
R
R
R
O
L
R
L
DT

## Slide 7: Thing Description -TDL Fragment
{
“@context”: ”http://example.org/tdl/tdl.jsonld”,
“@type”: “thing”
{
“@context”: ”http://example.org/tdl/professionalLighting.jsonld”,
“_thing”:
{“type”:”light”},
“_actions”: {
“brightness”: {
“change”: {  indexed in context, reference by “light.brightness.change”
“parameters”: [
{“name”: “targetValue”:
“type”:”brightnessValueType”},  TDL abstract types
{“name”: “transitionTime”,
“type”: “timeValueType”},
“bindings”: [
{“type”: ”ipso+coap”,
“describedBy”: “protocols.ipso+coap#light.level.change”}]
} } }
} }

## Slide 8: Binding for protocols.ipso+coap
“light”: {
“level”: {
“change”: {
“parameters”: [
{“name”: “targetValue”:
“datatype”:”decimal”,
“units”: “%”,
“range”: “0-100”},
{“name”: “transitionTime”,
“datatype”: “decimal”,
“units”: “s”} ],
“method”: ”post”,
“href”: “3001/0”,
“mediatype”: “application/senml+json”,
“expects”: {“template”: “{\“e\”:[
{\“n\”:\“5001\”,\“v\”:{targetValue}},
{\“n\”:\“5002\”,\“v\”:{transitionTime}}]}” },
“statusCodes”: [
{“code”: ”2.01”,
“status”: “success”},
{“code”: “4.04”,
“status” “failure”},
{“code”: “4.09”,
“status” “retry”} ]
} } }

## Slide 9: Questions and Follow On Work
What do the hypermedia descriptions of events, actions, and properties look like?
What are the functional abstractions that will be used to enable vertical specialization while still providing broad interoperability?
How does discovery integrate with API automation?
What are the metadata constructs for connecting constrained hypermedia to higher level abstractions?
Prototype using constrained lighting objects with LWM2M and IoT Toolkit open source python framework
Reference WoT client using Node-RED + extensions

## Slide 10: Deployment with LWM2M Devices
Web Applications
Common Client
ConstrainedDevices
Device Connector
Virtual Entity
Catalogs
Brokers
Pub-Sub
Discovery
M2M API
Pub-Sub
Hypermedia
Discovery
REST API
LWM2M
WoT Servient