## Slide 1: OCF Data Model
Michael J Koster

## Slide 2: OCF Resource Model
Resource model + Interaction model
CRUD+N mapped to RFC7252 CoAP
RFC6690 style hyperlinks with semantic annotation
Interface Types based on RFC6690 "if" link attribute
Resource Types based on RFC6690 "rt" link attribute

## Slide 3: Resource Structure
Links point to Resources
A resource has multiple Properties
rt and if are properties of all resources
Data and metadata, e.g. "value", "range", "units" are properties of a sensor resource
"links" property extends any resource to be a collection

## Slide 4: Example Resource Representation
{
"rt": ["oic.r.example", "oic.wk.col"],
"if": ["oic.if.s", "oic.if.r, oic.if.ll],
"value": 50,
"range": [0,100],
"units": "q/s"
"links" : [
{
"href": "http://example.org/description",
"rel": "describedby"
}
]
}

## Slide 5: Resource Type
Resource Type "rt" is a reference to a resource description
OCF Resource description uses RAML and JSON Schema
RAML defines allowable methods and Interface Types
JSON Schema defines payloads, properties, and data types

## Slide 6: Interface Type
OCF Interface Type "if" defines methods and payloads
A resource may expose more than one interface type
Each interface type may have different allowed methods
Each interface type may have different payloads
sensor, actuator, readonly, read/write, linklist, batch, and baseline types

## Slide 7: Resource Instance
A resource instance may expose more than one resource type and more than one interface type
The properties exposed are a function of resource type(s) and interface types

## Slide 8: Interaction Model
OCF URI reference includes query parameters to specify which resource type(s) and interface type(s) are to be transmitted/returned
URI Reference using OCF Scheme resolves to a protocol-specific URI
coaps://<auth>/<path>?<query>

## Slide 9: Interaction Model
GET /example/sensor?if=oic.if.baseline
{
"rt": ["oic.r.example", "oic.wk.col"],
"if": ["oic.if.s", "oic.if.r, oic.if.ll],
"value": 50,
"range": [0,100],
"units": "q/s"
"links" : [
{
"href": "http://example.org/description",
"rel": "describedby"
}
]
}

## Slide 10: Interaction Model
GET /example/sensor?if=oic.if.ll
{
"links" : [
{
"href": "http://example.org/description",
"rel": "describedby"
}
]
}

## Slide 11: Interaction Model
GET /example/sensor?if=oic.if.s
{
"value": 50,
}

## Slide 12: Interaction Model
GET /example/sensor?if=oic.if.r
{
"range": [0,100],
"units": "q/s"
}

## Slide 13: Interaction Model
GET /example/sensor?if=oic.if.s&if=oic.if.r
{
"range": [0,100],
"units": "q/s"
"value": 50,
}

## Slide 14: Batch Collection
GET /example/batch?if=oic.if.baseline
{
"rt": ["oic.r.example", "oic.wk.col"],
"if": ["oic.if.b", oic.if.ll],
"links" : [
{
"href": "temp",
"rt": ["oic.r.temperature"]
"if": ["oic.if.s"]
},
{
"href": "humid",
"rt": ["oic.r.humidity"]
"if": ["oic.if.s"]
}
]
}

## Slide 15: Batch Collection
GET /example/batch?if=oic.if.b
{
{
"href": "temp",
"rep": {
"temperature": 57
}
},
{
"href": "humid",
"rep": {
"humidity": 39
}
}
}

## Slide 16: RESTful Actuation
Use Batch Collection to model the target resources for actuation
Use Collection to create a container for RESTful Actuation, add to the Batch Collection
Actuation payload can be constructed in a way similar to a batch payload and applied to the Actuation resource

## Slide 17: RESTful Actuation
GET /example/light?if=oic.if.ll
{
"links" : [
{ "href": "switch",
"rt": ["oic.r.switch.binary"] },
{ "href": "brightness",
"rt": ["oic.r.brightness"] },
{ "href": "ct",
"rt": ["oic.r.colourtemperature"] },
{ "href": "ramptime",
"rt": ["oic.r.ramptime"] },
{ "href": "colorcontrol",
"rt": ["oic.r.actuation, oic.r.switch. binary", oic.r.brightness, oic.r.colourtemperature, oic.r.ramptime] },
]
}

## Slide 18: RESTful Actuation
POST /example/light/colorcontrol/?if=oic.if.a
{
"value": true,
"brightness": 80,
"ct": 3720,
"rampTime": 60
}

## Slide 19: /oic/res
Well known resource at /oic/res
Directory of resources on a device or bridge
RFC6690-like format list of links
Root of on-device resource discovery
Device REST API "entry point"
Also allows external resource directory

## Slide 20: Resource Definition
Uses RAML and JSON-Schema
RAML defines interfaces and methods
JSON-Schema defines payloads and data types
Oneiota tool is used to manage resource definitions at oneiota.org
Contains current OCF resource definitions
~90 Smart Home resource types registered in IANA CoRE Parameters Registry

## Slide 21: OCF Bridging and Mapping
Mapping of IEEE 11073 in progress
Mapping of Genivi VSS in progress
Mapping of UPnP device bridge in progress
Mapping of Allseen device bridge in progress
Bridging maps devices to OCF resource types using deep translation and OCF derived modeling
Many more Resource Types will be defined