## Slide 1: Issues for TPAC Plugfest
September 13th, 2017
Ryuichi Matsukura
Fujitsu Laboratories Ltd. / Fujitsu Ltd.
See IG issue #346, https://github.com/w3c/wot/issues/346

## Slide 2: Use Case (example)
New scenario: Two and more Servients collaborations, especially between the Internet and local networks
  Application on Smartphone connected to Internet can operate air conditioner on local network. Agent and gateway relay messages between application and device.
Remote controller
Electronic
appliance
Agent
Gateway

## Slide 3: Functional roles of WoT Servients
3 types of WoT Servients we suppose
  WoT Servient with ExposedThing, e.g. device
  WoT Servient with ConsumedThing, e.g. application
  WoT Servient with Exposed/ConsumedThing, e.g. gateway
Integration model
Serivent w/ C
Servient w/ CE
Servient w/ E
Serivent w/ C
Servient w/ CE
Servient w/ E
Servient w/ CE
application
gateway
device
application
gateway
(internet)
device
gateway
(local)
3-layer model
4-layer model
Bridge Servients on Internet and local

## Slide 4: Issues for TPAC plugfest
Interface between Servients
  Authentication
  Discovery and exchange TDs
  Firewall and NAT traversal
  Add “Event” operation for inter-Servient interface
Thing Description management
  Management
    How to create URI. A WoT Servient on the Internet cannot access Servients on local networks, because local Servients URI are assigned to the local address.
    Who and how to manage TDs. If many servients connect to networks, the management function is necessary to easily search TD someone want to connect.

## Slide 5: Call for participants
Please share the information of your Servients and legacy devices if you have a plan to participate.
Servient
(device)
Servient (device)
Servient
on local NW
Servient
on local NW
Servient
on Internet
Servient
(application)
Servient (application)
Legacy device
Legacy device
Firewall / NAT
Examples from past plugfest
Scripting runtime (Siemens, Nimura)
Node-RED (Matsukura)
Cloud gateway (Panasonic, Fujitsu)
Local gateway (Siemens, Fujitsu)
Air conditioner (Panasonic)
Blind (Fujitsu)