## Slide 1: Issues for TPAC Plugfest
September 20th, 2017
Ryuichi Matsukura
Fujitsu Laboratories Ltd. / Fujitsu Ltd.
See IG issue #346, https://github.com/w3c/wot/issues/346

## Slide 2: Use Case (example)
New scenario: Two and more Servients collaborations, especially between the Internet and local networks
  Application on Smartphone connected to Internet can operate air conditioner on local network. Agent and gateway relay messages between application and device.
Remote controller
Electronic
appliance
Agent
Gateway

## Slide 3: Functional roles of WoT Servients
3 types of WoT Servients we suppose
  WoT Servient with ExposedThing, e.g. device
  WoT Servient with ConsumedThing, e.g. application
  WoT Servient with Exposed/ConsumedThing, e.g. gateway
Integration model
3-layer model
4-layer model
Serivent w/ C
Servient w/ CE
Servient w/ E
application
gateway
device
Serivent w/ C
Servient w/ CE
Servient w/ E
Servient w/ CE
application
gateway
(internet)
device
gateway
(local)
Bridge Servients on Internet and local

## Slide 4: Issues for TPAC plugfest
Interface between Servients
  Authentication
  Discovery and exchange TDs
  Firewall and NAT traversal
  Add “Event” operation for inter-Servient interface
Thing Description management
  Management
    How to create URI. A WoT Servient on the Internet cannot access Servients on local networks, because local Servients URI are assigned to the local address.
    Who and how to manage TDs. If many servients connect to networks, the management function is necessary to easily search TD someone want to connect.

## Slide 5: Call for participants
Please share the information of your Servients and legacy devices if you have a plan to participate.
Servient
(device)
Servient (device)
Servient
on local NW
Servient
on local NW
Servient
on Internet
Servient
(application)
Servient (application)
Legacy device
Legacy device
Firewall / NAT
Examples from past plugfest
Scripting runtime (Siemens, Fujitsu)
Node-RED (Fujitsu)
Cloud gateway (Panasonic, Fujitsu)
Local gateway (Siemens, Fujitsu)
Air conditioner (Panasonic)
BACnet device (Siemens)
OCF device (Intel)
Lemonbeat device? (Lemonbeat)
IPSO device (SmartThings)
Blind, LED light (Fujitsu)

## Slide 6: Additional specifications for plugfest (overview)
Architecture (integration model)
Sequence diagrams among Servients
Inter-Servient Interface
  Authentication : ACE (see in Current Practice)
  Discovery and exchange TD : NEW
  Firewall and NAT traversal : NEW
  “Event” operation with subscription : NEW
TD Management
  Life cycle management
  URL naming convention

## Slide 7: Basic sequence diagram (1 of 4)
Shows interaction example between Servients
  Authentication
  Discovery/Register & Lookup
Register w/ TD
OK
Look up thing
OK w/ TD
Authentication
Authentication
Servient w/ E
Servient w/ CE
Servient w/ C

## Slide 8: Basic sequence diagram (2 of 4)
  “Set” operation
  “Get” operation
Servient w/ E
Servient w/ CE
Servient w/ C
Get w/ property
Get w/ property
OK w/ value
OK w/ value
Set w/ property
Set w/ property
OK
OK

## Slide 9: Basic sequence diagram (3 of 4)
  “Subscribe” operation
  “Event” operation
Servient w/ E
Servient w/ CE
Servient w/ C
Subscribe
Subscribe
OK
OK
Event
Event
Unsubscribe
Unsubscribe
OK
OK
Event
Event
…
…

## Slide 10: Basic sequence diagram (4 of 4)
  Delete TD
  Deauthentication
Servient w/ E
Servient w/ CE
Servient w/ C
Unregister w/ TD
OK
Delete w/ TD
OK
Deauthentication
OK
Deauthentication
OK

## Slide 11: Authentication
IETF ACE
Best practice 8 described in Current Practice

## Slide 12: Discovery and delivery of TD
2 Diagrams of PlugFest setting
  (1) the one in the past and (2) the expected next version at TPAC
Need for TD management in the future
Servient
(device)
Servient
(device)
Servient
(app)
Servient
(gateway)
Servient
(app)
Servient
(device)
Servient
(app)
url=http;//192.168.0.1/LED
(1)Broadcast TD(device) to others
url=http;//192.168.0.1/LED
(1)Broadcast TD(device) to gateway
(2)Lookup TD(device) to gateway
Same network that broadcast packet can reach
Two networks that broadcast packet cannot reach
(1) Diagram for the past plugfest
(2) Diagram for the next plugfest
Broadcast packet cannot reach
TD repo.

## Slide 13: Need for managing multiple Servients
Internet
Servient
(Device1)
Servient
(Local Gateway)
Servient
(Local
Application1)
Servient
(Device2)
Servient
(Cloud Gateway)
Servient
(Device3)
Servient
(Local Gateway)
Servient
(device4)
Servient
(Cloud Application1)
Servient
(Cloud
Application2)
Firewall/NAT
Firewall/NAT
url=http;//192.168.0.1/LED
(1)Send TD(device) to cloud gateway
(2)Lookup TD (device) to cloud gateway
ISSUE: The URL of the local Device 4 below (url=192.168.0.1/LED)
is not available for the remote Applications.
Need to identify the URL of the local Devices from the remote side
How to generate URI
How to deliver the TD to the other side
How to search the TD
Point 1: Need to manage multiple Servients for multiple Applications on the remote side
Point 2: Need to manage multiple Servients for multiple Devices on the local side
TD repo.
Local side:
Remote side:

## Slide 14: NAT Traversal
TBD

## Slide 15: Need to collaborate
Architecture TF
  Add the integration model and the roles of Servients
  Sequence diagrams for the interactions: “authentication”, “read”, “write”, “subscribe”, and “event”.
Thing Description TF
  Discovery and exchange TD
  TD management