## Slide 1
VSSo: a car signal ontology
April 18, 2018 | Extension of the Vehicle Signal Specification
Benjamin Klotz
PhD student, BMW Group, EURECOM

## Slide 2: Initial context
Front camera
Radar
Tire pressure sensor
Park assistant
Steering angle sensor
Wheel speed sensor
Blind spot detection
Adaptive cruise control
Temperature sensor
Oil temperature sensor
Vehicle height sensor
Adapt infotainment from online use favorite playlists and volume.
Drive your car in front of the building you are leaving
…
{"name":"accelerator_pedal_position","value":0,"timestamp":1361454211.483000}
{"name":"fuel_level","value":23.478279,"timestamp":1361454211.485000}
{"name":"torque_at_transmission","value":1,"timestamp":1361454211.488000}

## Slide 3: Driving context
Signal data model
Driving Contexts
Web services
Smart home
Smart city
Goals:
Personalization
Awareness
Data fusion
…

## Slide 4: Enabling interoperability through the signal data model?

## Slide 5: VSS in a nutshell
Figure:
451 branches
1103 leaves:
  43 attributes
  1060 signals: including
    (700 seat-related),
    268 with unit
Signal/Attribute
Body
Raindetection
Intensity
ADAS
Type: UInt8
Unit: percent
Description: “…”
Value: restriction or free
Cabin
Chassis
Drivetrain
OBD
Vehicle
Weight
Attribute
Signal
Signal entries
Examples:
Gearbox-sensed speed: .Drivetrain.Transmission.Speed
Engine speed: .Drivetrain.Engine.Speed
GPS-sensed speed: .Cabin.Infotainment.Speed
Left door lock: .Body.Row1.Door.Left.IsLocked
Right mirror tilt: .Cabin.Mirror.Right.Tilt

## Slide 6: Ontologies for (car) signals [1]
The Semantic Sensor Network (SSN) ontology
is an ontology for describing
sensors
and their observations,
the involved procedures,
the studied features of interest,
the samples used to do so,
and the observed properties,
as well as actuators, actuations...
[1] https://www.w3.org/TR/vocab-ssn/
SSN follows a horizontal and vertical modularization architecture by including a lightweight but self-contained core ontology called SOSA (Sensor, Observation, Sample, and Actuator) for its elementary classes and properties.
A W3C and OGC recommendation (19 October 2017)
Supports a wide range of applications and use cases, including satellite imagery, large-scale scientific monitoring, industrial and household infrastructures, social sensing, citizen science, observation-driven ontology engineering, and the Web of Things.

## Slide 7: SOSA/SSN observation & sensor pattern
sosa:ObservableProperty
sosa:Sensor
sosa:Observation
sosa:madeBySensor
sosa:isObservedBy
sosa:observedProperty
rdf:type
rdf:type
sosa:Result
sosa:hasResult
rdf:type
22,2km/h^^cdt:speed
22,2^^xsd:double
qudt:KilometerPerHour
qudt:numericValue
qudt:unit
sosa:hasSimpleResult
sosa:phenomenonTime
geo:lat
geo:lon
:Speed
Definition of a signal
Definition of a sensor
Well-defined units
Geolocation
No formal definition of:
“speed” or other observable properties
“speedometer” or other car sensors/actuators
“Car” or vehicle parts
BUT
"2018-04-18T13:36:12Z"^^xsd:dateTime
48.1374300° 11.5754900°

## Slide 8: SSN/SOSA with a VSS ontology
sosa:ObservableProperty
sosa:Sensor
sosa:Observation
sosa:madeBySensor
sosa:isObservedBy
sosa:observedProperty
:Speed
rdf:type
sosa:Result
sosa:hasResult
rdf:type
22,2km/h^^cdt:UCUM
22,2^^xsd:double
qudt:Unit
qudt:numericValue
qudt:unit
sosa:hasSimple
Result
vss:Speedometer
vss:Speed
vss:ObservableSignal
rdfs:subClassOf
rdfs:subClassOf
rdfs:subClassOf
vss:Transmission
vss:Drivetrain
vss:InternalCombustion
vss:partOf
vss:partOf
vss:hasSignal
vss:Branch
rdfs:subClassOf
rdfs:subClassOf
rdfs:subClassOf
4Nm^^cdt:torque
vss:maxTorque
rdf:type

## Slide 9: What is required ?

## Slide 10: From VSS spec to the VSS ontology
VSS
Add sensors and actuators
Map to existing Ontologies
- SSN/SOSA
- QUDT (unit)
Apply consistency policies
Generate definition of VSS concepts
Manually validate and clean the generated ontology
VSSontology
Modeling policies
VSS concepts have unique names
All signals are either observable, actuable or both
All signals have either a sensor or an actuator
All branches are part of the top “vss:Vehicle” branch
All position-dependent branches have a property “position”

## Slide 11: Modeling choice 1: unique names for unique concepts
Some signals represent the same phenomenon, sensed by different sensors
  Ex: Drivetrain.Speed (sensed by the gearbox) and Infotainment.Speed (sensed by the GPS)
vss:VehicleSpeed
vss:ObservableSignal
vss:Transmission
vss:hasSignal
vss:Branch
rdfs:subClassOf
vss:Infotainment
rdfs:subClassOf
vss:hasSignal
rdfs:subClassOf
sosa:Sensor
vss:Speedometer
vss:GPS
rdfs:subClassOf
rdfs:subClassOf
sosa:isObservedBy
sosa:isObservedBy
“vss:VehicleSpeed” is a unique phenomenon
observed by different sensors
  Producing different signals
Names are clarified to avoid homonymy

## Slide 12: Modeling choice 2: signals are observable, actuable or both
Some signals are attached to sensors, other to actuators, or both. For instance
  Drivetrain.Transmission.Speed observes a speedometer
  Mirror.Right.Heating only acts on a heater
  Infotainment.Media.Volume observes/acts on the media volume
Page 12
sosa:ObservableProperty
sosa:Sensor
sosa:Observation
sosa:madeBySensor
sosa:isObservedBy
sosa:observedProperty
sosa:ActuableProperty
sosa:Actuator
sosa:Actuation
sosa:madeByActuator
sosa:isActedBy
sosa:actsOnProperty
rdfs:subClassOf
rdfs:subClassOf
vss:ActuableSignal
vss:ObservableSignal
rdfs:subClassOf
vss:VehicleSpeed
vss:Heating
vss:MediaVolume
rdfs:subClassOf

## Slide 13: Modeling choice 3: all signals have a sensor or actuator
vss:VehicleSpeed
vss:ObservableSignal
vss:Transmission
vss:Branch
rdfs:subClassOf
sosa:Sensor
vss:Speedometer
rdfs:subClassOf
vss:Vehicle
vss:partOf
rdfs:subClassOf
Signals
Sensors/Actuators
Branches and parts
Produced by [sensor]
Consumed by [actuator]
Contains (vss:partOf)
vss:hasSignal

## Slide 14: Modeling choice 4: all branches are vss:partOf vss:Vehicle
vss:partOf
vss:Vehicle
vss:Body
vss:ADAS
vss:Cabin
vss:Chassis
vss:Drivetrain
vss:OBD
vss:Branch
rdfs:subClassOf
Signal
Body
ADAS
Cabin
Chassis
Drivetrain
OBD
Vehicle
Current VSS structure
VSSontology structure

## Slide 15: Modeling choice 5: position ≠ branch
Ex: Door.Left.IsLocked, Mirror.Right.Tilt
Branches vss:Door and vss:Mirror have vss:hasPosition property with limited potential values (“Left”,”Right”,”Row1”, …)
rdf:type
vss:DoorIsLocked
rdfs:subClassOf
vss:Door
vss:Mirror
vss:hasSignal
vss:Branch
rdfs:subClassOf
rdfs:subClassOf
:LeftDoorLock
vss:MirrorTilt
rdfs:subClassOf
vss:hasSignal
:RightMirrorTilt
rdf:type
vss:hasPosition
“Left”^^cdt
“Right”^^cdt
:Door2
:Mirror3
vss:Signal
vss:hasPosition
rdf:type
rdf:type
Branch
Position

## Slide 16: Application: linking signals to a heterogeneous context
vso:Automobile
Aggressive behavior
Neutral
Safe behavior
Traffic jam
Close event
Closed road
Driving Contexts
Web services
Smart home
Smart city

## Slide 17: What about OEM-specific concepts ?

## Slide 18: Ontological specification
84 formally-defined vehicle parts
~300 formally-defined signals
~40 formally-defined attributes
VSSo
cookbook
Ontological specification
Base VSSo

## Slide 19: VSS private branch
Private branch
OEM-specific concepts
Extension of VSS
Merged into VSS when generating specifications
Private OEM-specific ontology cookbook:
Write VSS-compliant specification of private concepts (new signals, attributes and branches)
  Follow the VSS policies just as when creating a private branch
Generate the ontology using the existing tool
Validate the ontology
  Check the unicity of concepts and definitions (in the private branch and if possible with VSSo)
Define a private namespace for your ontology integrating VSSo

## Slide 20: Do you have questions ?
Thank you for your attention

## Slide 21: Branch examples
vss:Branch a rdfs:Class, owl:Class;
rdfs:label "Branch"@en;
rdfs:comment "Branch of the vehicle. Either a component (Body, Chassis...) or the complete vehicle"@en.
vss:ObstacleDetection a rdfs:Class, owl:Class;
rdfs:subClassOf vss:Branch;
rdfs:label "ObstacleDetection"@en;
rdfs:comment "Signal/Attribute.ADAS.ObstacleDetection : Signals form Obstacle Sensor System"@en;
rdfs:subClassOf [
a owl:Restriction;
owl:onProperty vss:partOf;
owl:allValuesFrom vss:ADAS
];
rdfs:subClassOf [
a owl:Restriction;
owl:onProperty vss:hasSignal;
owl:allValuesFrom [owl:unionOf vss:ObstacleDetectionIsActive, vss:ObstacleDetectionError]
].

## Slide 22: Signal examples
vss:ObservableSignal a rdfs:Class, owl:Class;
rdfs:subClassOf sosa:ObservableProperty;
rdfs:label "Observable signal"@en;
rdfs:comment "All observable signals that can dynamically be updated by the vehicle"@en.
vss:AmbientAirTemperature a rdfs:Class, owl:Class;
rdfs:subClassOf vss:ObservableSignal;
rdfs:label "AmbientAirTemperature"@en;
rdfs:comment "Signal.Vehicle.AmbientAirTemperature : Ambient air temperature"@en;
rdfs:subClassOf [
a owl:Restriction;
owl:onProperty sosa:isObservedBy;
owl:allValuesFrom vss:Thermometer
];
rdfs:subClassOf [
a owl:Restriction;
owl:onProperty qudt:unit;
owl:allValuesFrom vocab:DegreeCelcius
].

## Slide 23: Signal examples
vss:attribute a owl:ObjectProperty;
rdfs:label "Attribute"@en;
rdfs:comment "Attribute signals that do not change during the power cycle of a vehicle."@en;
rdfs:domain vss:Branch.
vss:driveType a owl:DatatypeProperty;
rdfs:subPropertyOf vss:attribute;
rdfs:label "DriveType"@en;
rdfs:comment "Attribute.Drivetrain.Transmission.DriveType : Drive type."@en;
rdfs:domain vss:Transmission;
rdfs:range [owl:oneOf("unknown"@en "Front-wheel drive"@en "Rear-wheel drive"@en
"All-wheel drive"@en)].

## Slide 24: Thank you!
Visit GENIVI at http://www.genivi.org or http://projects.genivi.org
Contact us: help@genivi.org
GENIVI is a registered trademark of the GENIVI Alliance in the USA and other countries. Copyright © GENIVI Alliance 2017.