The request IRI is constructed as follows:

- The local name in a template SHOULD match at least one element from the instance data of the input message.† When there is no match, the template is replaced by an empty string. Otherwise, the template consumes the first non-consumed matching element from the instance data. The next occurrence of the template consumes the next non-consumed matching element, and so on until all templates are processed. Matching elements are consumed in the order in which they appear in the instance data.  Cited elements (i.e. elements referenced in templates) MUST NOT carry an xs:nil attribute whose value is "true"†.

- Each raw template (rawTemplate production in the grammar above) is replaced by the possibly empty single value of the corresponding element from the instance data. No percent-encoding is performed.

- Each encoded template (encodedTemplate production in the grammar above) NOT preceded in the {http location} property by a "?" or a "#" character is replaced by the possibly empty single value of the corresponding element from the instance data.  All characters EXCEPT the following ones MUST be percent-encoded:

  - ALPHA | DIGIT | "-" | "." | "_" | "~" | "!" | "$" | "'" | "(" | ")" | "*" | "+" | "," | ";" | "=" | ":" | "@".

- Each encoded template (encodedTemplate production in the grammar above) preceded in the {http location} property by a "?" or a "#" character is replaced by the possibly empty single value of the corresponding element from the instance data.  All the following characters MUST be percent-encoded:

  - The value of the {http query parameter separator} property, if present, otherwise the value of the {http query parameter separator default} property.

  - The other characters, EXCEPT the ones in the range: ALPHA | DIGIT | "-" | "." | "_" | "~" | "!" | "$" | "'" | "(" | ")" | "*" | "+" | "," | ";" | "=" | ":" | "@" | "?" | "/".

- Each uncited element (i.e. each element not referenced in a template) to be serialized, if any, is encoded as for an encoded template.

- Percent-encoding MUST be performed using the UTF-8 representation of the character as prescribed by section 6.4 of [IETF RFC 3987].

- Each double curly brace (openBrace or closeBrace production in the grammar above) is replaced by a single literal curly brace ("{" or "}" respectively). This provides a simple escaping mechanism.